## Slide 1: Introduction to Networks and Wireshark
Overview of Networking

## Slide 2: What is a Network?
When you connect two or more computers or devices, you have “networked” them together
Networks can use wires and radio waves (wi-fi)
Usually, you want or need more than two devices talking to each other
  Introduce more networking hardware to help
  A router symbol shows both wired and wireless network

## Slide 3: Speaking the Same Language
Information exchange must be done so that all parties can understand the information being shared
What happens if you show up to a class and your teacher is speaking Korean and you only know French? How well does that information exchange work?
There has to be an agreement on the language used for exchanging human information
Computers are the same – they need to agree on how to exchange information
  These network protocols provide a common “language” for how to communicate

## Slide 4: Network Protocols
Definition: A set of rules that governs the connection of computer systems to the internet (Oxford Dictionary)
Ever heard of TCP/IP?
  TCP = Transmission Control Protocol
  IP = Internet Protocol
The two protocols are used together to establish and maintain a network conversation
TCP focuses on establishing and maintaining a network connection
  Connection-oriented, knows if a packet is missing
IP defines how computers send packets of data to each other

## Slide 5: Network Protocols – Continued
In addition to TCP, there is UDP
  UDP = User Datagram Protocol
  Unlike TCP, UDP doesn't guarantee that the packets will get to the right destinations.
  UDP uses IP (Internet Protocol) as well
UDP is connection-less
UDP is less reliable than TCP
  Relies on devices in between the sending and receiving computers to correctly get the data where it's supposed to go

## Slide 6: Network Traffic
Packets on a network are pieces of a file that sent over the network and re-assembled on the receiving side.
Imagine the network is a straw and you want to push through a sandwich.
How do you do it? One small piece (packet) at a time.
“Straw” - Network

## Slide 7: Network Data Packets Concept Map
Network
Individual Packet
Original Image
Image divided up into packet-sized data pieces
IP sends packet to network
internet
Packets get sent to destination

## Slide 8: IP Addresses
How does a packet know where it came from and where it’s going to?
Just like a letter, is uses addresses.
Source Address - the IP address of where it’s coming from (like a return address)
Destination Address – the IP address of where it’s going to
Source Address
Destination Address

## Slide 9: IP Addresses
How does a packet know where it came from and where it’s going to?
Just like a letter, is uses addresses.
Source Address - the IP address of where it’s coming from (like a return address)
Destination Address – the IP address of where it’s going to
Source Address
Destination Address
10.0.0.15
93.184.216.34

## Slide 10: Other Identifiers – The MAC Address
Computers are assigned IP addresses through software (changeable)
The hardware has its own identifier, MAC address (non-changeable)
Assigned at manufacture time, the first three bytes map to manufacturer (OUI listing)
Can tell information about network hardware connected through the network traffic. The MAC address has (leaks) this information
MAC addresses can be spoofed (faked), but generally the way to identify a specific physical network device
Notes: Image from https://learntomato.flashrouters.com/what-is-a-mac-address-how-to-find-my-mac-address/

## Slide 11: Not Lost in Translation
How do you get from “example.com” to the IP address 93.184.216.34?
  Answer: the Domain Name System (DNS)!
DNS is like a phonebook for domain names mapped to IP addresses.
Notes: Image from https://tibbbz.medium.com/pi-hole-dns-for-dummies-5763b65ee527

## Slide 12: Ports
Network ports indicate what type of service it is (email, file transfer, web).
Typical ports used when browsing the internet
  Resolving a URL (www.example.com) to an IP address (198.41.0.4) uses the Domain Name System (DNS) on port 53
  Unencrypted website traffic (HTTP) – Port 80
  Encrypted website traffic (HTTPS) – Port 443
Port Number | Usage
23 | Telnet - Remote login service, unencrypted text messages
25 | Simple Mail Transfer Protocol (SMTP) E-mail Routing
53 | Domain Name System (DNS) service
80 | Hypertext Transfer Protocol (HTTP) used in World Wide Web
110 | Post Office Protocol (POP3) used by e-mail clients to retrieve e-mail from a server
123 | Network Time Protocol (NTP)
143 | Internet Message Access Protocol (IMAP) Management of Digital Mail
161 | Simple Network Management Protocol (SNMP)
194 | Internet Relay Chat (IRC)
443 | HTTP Secure (HTTPS) HTTP over TLS/SSL
Notes: Note about DNS. In the prior slide, the source and destination addresses are IP addresses.
Using TCP/IP, you can’t directly “go” to example.com. That first needs to use DNS to lookup the IP address, and then the request for the content at 198.41.0.4 is transmitted.

## Slide 13: Do you think it’s possible to analyze data sent over the network?
Notes: Yes! This is done for troubleshooting, performance measurements, and for security monitoring.

## Slide 14: Wireshark
Wireshark is a powerful analysis software that allows you to not only capture network and device packets, but to analyze them too (i.e., a packet analyzer).
  Remember - A packet is a fragment of data that is sent over a network from one machine to another. This data usually includes a source port, source IP address, destination port, destination IP, and other data that we will see in this lab.
Wireshark allows a user to analyze the traffic traveling in and out of the machine, which can serve many uses.
© 2020 Virginia Cyber Range. Created by Thomas Weeks. (CC BY-NC-SA 4.0)

## Slide 15: Wireshark
© 2020 Virginia Cyber Range. Created by Thomas Weeks. (CC BY-NC-SA 4.0)

## Slide 16: Attack of the Sharks
≠

## Slide 17: Why Use Wireshark?
Troubleshoot network connections.
Filter data between two hosts to see a single network “conversation.”
Comparing all “conversations” to discover bad actors or “bandwidth hogs.”
Filter captured data to analyze specific protocols and ports being used.
Analyze specific statistics about the traffic coming in and out of the system.
Adapted from © 2020 Virginia Cyber Range. Created by Thomas Weeks. (CC BY-NC-SA 4.0)

## Slide 18: Wireshark Lab
Wireshark allows you to view pieces of data (called packets) in real-time as they go in and out of a system and can be saved as packet capture or pcap files.
In this lab, you will be analyzing packet capture files (network forensics).
The objectives at the end of the lab is understand:
  Wireshark overview
  Analyzing DNS Packets
  Name-to-IP address resolution
  Wireless access points and identifiers

## Slide 19: Debrief